## Slide 1
URJA AI
v2.0
Network-Topology-Aware
Energy Intelligence Platform
AI-Powered Electricity Theft Detection & Revenue Recovery for BESCOM, Bengaluru
Lead Dev: Yeshwanth Reddy P G · Researcher: Aditya S · Debugger: Bezaleel Paul N
CMR University · 1st Year CSE / AI-ML · PAN IIT AI for Bharat 2026 · Theme 8 · BESCOM
15
DTs Monitored
45
Days of Data
3
Anomalies Found
0
False Positives

## Slide 2
The Problem — Why BESCOM Bleeds Revenue
India's AT&C losses cost utilities ₹50,000+ Crore annually
26.5%
National Average AT&C Loss
Aggregate Technical & Commercial losses across India's distribution utilities
₹50,000 Cr+
annually in losses
Every 1% AT&C loss reduction = direct revenue recovery
Theft & Bypass
Direct meter bypass at night — entirely invisible to existing systems
Meter Tampering
Meters manipulated to under-read by 30–70% from a specific date
Unbilled Connections
Illegal connections drawing constant load with zero billing record
Inspector Alert Fatigue
100s of low-confidence alerts daily — inspectors stop responding within weeks
Aging Transformer Noise
Old DTs misclassified as fraud, sending inspectors on futile visits

## Slide 3
The Core Insight — Energy Forensics
Why physics separates fraud from technical loss using a single linear regression
Technical Loss (I²R Physics)
Loss scales with load SQUARED
→ High load = more heat loss in wires
→ Loss% correlates perfectly with load level
→ R² close to 1.0 in regression
→ Intercept stays small (<3%)
Commercial Loss (Fraud)
Bypass steals a FIXED amount daily
→ 200 kWh stolen at 30% or 90% feeder load
→ Loss becomes load-INDEPENDENT
→ R² collapses toward zero
→ Intercept jumps high (>10%+)
5 lines of scipy.stats.linregress
= the entire detection algorithm
What R² + Intercept Tells You
R² > 0.70
Intercept < 3%
TECHNICAL_CLEAN
I²R physics only. No action.
R² < 0.30
Intercept > 8%
COMMERCIAL_DOMINANT
Load-independent. Investigate.
Night/Day ratio
> 20×
BYPASS_SIGNATURE
CRITICAL. Night inspection.
Step change
+5.65% Day 15
NEW_TAMPER_EVENT
HIGH. Daytime meter audit.
R² > 0.86
Intercept 80%+
COMMERCIAL_DOMINANT
Unbilled connection. Inspect.

## Slide 4
System Architecture — 6-Layer Hardened Pipeline
Each layer independently testable · No silent failures · All signals typed and logged
L1
Data Quality
& Clock Sync Gate
6-class reading classifier: VALID / SUSPECT_SPIKE / MISSING / DROPOUT / PREPAID_DEPLETION / NEGATIVE
L2
Asset-Aware
Baseline Correction
DT age factor + power factor correction per consumer type. Aging DTs get separate intercept baseline.
L3
Network Energy
Balance Engine
Loss = DT Input − ΣMeters. Computed every 15 minutes. Cohort-median imputation for dead meters.
L4
Loss Fingerprinting
Engine (Core)
Per-DT linear regression over 30-day window. R² + intercept + night-peak → 5-pattern taxonomy.
L5
STL + LightGBM
Demand Forecasting
STL decomposition → LightGBM on residuals. 12 features. SHAP pre-cached. 24h headroom score per DT.
L6
Inspector Priority
Queue Generator
Revenue-ranked dispatch. log1p scoring. Separate inspection vs maintenance queues. Evidence briefs.

## Slide 5
Synthetic Network — generate_data.py
259,200 realistic meter readings · 3 feeders · 15 DTs · 60 meters · 45 days
259K
Total Readings
15
DTs
60
Smart Meters
4,320
Slots/Meter
3
Anomalies Planted
Network Topology
▸ F_JAYANAGAR
5 DTs · RESIDENTIAL heavy · age 6–20yr
▸ F_BTM
5 DTs · COMMERCIAL_LIGHT + HEAVY · age 3–18yr
▸ F_KORAMANGALA
5 DTs · MIXED · age 7–22yr · holds all 3 anomalies
Load Profile Models
RESIDENTIAL — morning + evening peaks, April AC surge +25%
COMMERCIAL_LIGHT — 9am–9pm, weekends -30%
COMMERCIAL_HEAVY — 3-shift pattern (0.6/0.85/1.0 factor)
Tech loss = I²R(load²) + core 1.5% + age factor
Planted Anomaly Specifications
A1 — BYPASS_SIGNATURE BTMSTG-DT-14 · 3 meters × 45% reduction · 10pm–4am nightly · Commercial-Light DT
A2 — NEW_TAMPER_EVENT JAYNGR-DT-07 · 1 meter reads 70% of real value · from Day 15 forward only
A3 — COMMERCIAL_DOMINANT KORAMGLA-DT-22 · +2.5 kWh/slot constant unbilled load on DT input · no matching meter

## Slide 6
Loss Fingerprinting Engine — The 5-Line Algorithm
Explainability beats black-box ML — any field engineer can verify this on a whiteboard
Core Regression
corrected_loss = loss_pct − age_factor − pf_factor
slope, intercept, r_value, p_value, std_err =
linregress(dt_input_kwh, corrected_loss)
r_squared = r_value ** 2
→ Classify into 5 patterns using R², intercept, night_peak, step_change
Hardening Guards (v2.0)
✓ Load variance check: peak/valley ≥ 2× before running regression
✓ Night-peak flag: night > day × 1.3 AND night > 5% absolute
✓ Step detection on full 45-day window, relative threshold: max(3%, 30% × first-half intercept)
✓ 4-condition gate: avg_corrected >6%, intercept >6%, feeder imbalance, revenue materiality
✓ SHAP values cast to np.float64 before JSON serialisation — no dtype crashes
5-Pattern Taxonomy
BYPASS_SIGNATURE
Night peak>20× + intercept>10%
→ CRITICAL · Night visit
NEW_TAMPER_EVENT
Step jump >30% of baseline
→ HIGH · Daytime audit
COMMERCIAL_DOMINANT
R²>0.70 + intercept>20%
→ HIGH · Unbilled connection
AGING_TRANSFORMER
Age>15 + intercept 2.5–6%
→ MAINTENANCE · Replace DT
TECHNICAL_CLEAN
Low intercept, no fraud signal
→ LOW · Monitor only

## Slide 7
Detection Results — All 3 Anomalies Found
CRITICAL ranked #1 via log1p scoring · Revenue in rupee ranges · Zero false positives
RANK 1 · CRITICAL
BTMSTG-DT-14
BYPASS SIGNATURE
R²:
0.34
Intercept:
20.93%
Night/Day:
20× ratio
Revenue:
₹1,847–₹2,499/mo
Visit:
Night 10pm–2am
Persistent:
15 days
Night-peak physically impossible without bypass wiring. All 4 conditions met.
RANK 2 · HIGH
KORAMGLA-DT-22
COMMERCIAL DOMINANT
R²:
0.86
Intercept:
80.57%
Night/Day:
Load-correlated
Revenue:
₹26,534–₹35,900/mo
Visit:
Daytime 10am–4pm
Persistent:
45 days
High R² + enormous intercept = constant unbilled load perfectly correlated with feeder.
RANK 3 · HIGH
JAYNGR-DT-07
NEW TAMPER EVENT
R²:
0.02
Intercept:
10.06%
Step Change:
+5.65%
Revenue:
₹3,631–₹4,912/mo
Visit:
Daytime 10am–4pm
Persistent:
30 days
Step intercept jump from Day 15. 45-day window confirms pre/post regression divergence.
MAINTENANCE — JAYNGR-DT-04 (age 20yr) + KORAMGLA-DT-21 (age 22yr) · Intercept 3.25% vs clean baseline 1.2% · Correctly routed to transformer replacement queue, NOT inspection

## Slide 8
L5 — STL + LightGBM Demand Forecasting
Seasonal decomposition before ML · 12-feature engineering · SHAP pre-cached · Headroom scoring
Why STL First?
STL separates the load series into 4 components:
• Trend (slow-moving baseline)
• Weekly seasonality
• Daily seasonality
• Residual ← LightGBM trains on this
LightGBM learns anomalies and short-term deviations, not repeating patterns it would overfit to.
Cold-Start Protocol
DTs with <21 days history: proxy forecast from nearest 3 similar DTs by consumer type. Labelled PROXY FORECAST in UI. Cannot reach HIGH priority until 21-day native window completes.
Feature Engineering (12 features)
→ Time: hour, day-of-week, month, slot (0–95), is_weekend, is_holiday (Karnataka calendar)
→ Lag: load at t-1h, t-24h, t-168h (same slot last week)
→ Rolling: 24h mean + std, 7-day rolling mean
SHAP Explainability
All SHAP values pre-computed and cached to disk before demo. np.float64 cast ensures JSON safety. Never computed live — zero latency risk during presentation.
Headroom = (DT Capacity − Forecasted Peak) / Capacity
→ RED <15% · AMBER 15–30% · GREEN >30%
15 LightGBM models · 80/20 time-stratified split · Early stopping at 10 rounds

## Slide 9
Inspector Priority Queue — Revenue-Ranked Dispatch
log1p scoring prevents revenue bias · Pattern-aware visit times · Separate maintenance queue
Chart: Monthly Revenue Loss Estimate (₹)
| DT-22 Unbilled | DT-07 Tamper | DT-14 Bypass
Low Estimate | 26534 | 3631 | 1847
High Estimate | 35900 | 4912 | 2499
Queue Scoring Formula
score =
priority_weight (CRITICAL=100)
+ min(50, log1p(rev_high))
+ min(20, days_persistent)
log1p: CRITICAL bypass stays #1
even with lower rupee value.
Inspection Queue
CRITICAL + HIGH fraud patterns
Bypass = night visit · Others = daytime
Maintenance Queue
AGING_TRANSFORMER pattern
Revenue = ₹0 (physics, not recoverable)
Total Recoverable (Inspection Only): ₹31,312–₹43,311/mo · ₹3.75L–₹5.2L/year

## Slide 10
Streamlit Demo App — 4-Page Intelligence Dashboard
Dark-theme · Pattern-driven explanations · All values computed live from fingerprinting results
📍 Zone Risk Map
· Plotly Scattermap: 15 DTs color-coded CRITICAL→red, MAINTENANCE→blue
· 5-column KPI row all computed live from fp_df and queue_df
· DT Status Summary table: MAINTENANCE cells blue, CRITICAL red
· Hover tooltip: pattern, avg loss%, rev estimate, priority label
🚨 Inspector Queue
· Revenue-ranked cards — CRITICAL always #1 via log1p scoring
· Evidence string (130 char max): R², night-peak, step change, days
· Maintenance Queue: aging DTs labelled 'not recoverable by inspection'
· Demo Validation: confirms all 3 planted anomalies detected with rank
🔬 DT Drill-Down
· Loss-Load Scatter: regression line overlay, night readings red-highlighted
· Time-Series: daily avg loss% · anomaly markers from data_start (not hardcoded)
· Pattern-based explanation block driven by fingerprinting engine
· Evidence captions: night-peak (BYPASS only) · step change magnitude
📊 Loss Scatter
· R² vs Intercept scatter for all 15 DTs — the fingerprint map
· Color by priority · marker_size clipped ≥4 to prevent negative size crash
· Fraud zone (top-left) vs Technical zone (bottom-right) annotations
· Explainer panel: how to read R² + intercept for judges and BESCOM staff

## Slide 11
11 Loopholes Identified & Systematically Resolved
Adversarial analysis: hostile jury + BESCOM field engineer + competing team perspective
L01
Clock Sync Noise
1hr rolling avg for high-variance DTs · materiality floor per DT
L02
PF — Industrial DTs
Consumer-type tag + PF correction · PF-UNCERTAIN raises evidence threshold
L03
Seasonal Regime Shifts
Persistence extends 21→35 days during April AC surge season
L04
Cohort Too Small
Min 15 meters required · fallback feeder+type → zone+type
L05
Aging Mimics Fraud
Age+intercept+no night_peak → MAINTENANCE queue, not inspection
L06
Flat Tariff Revenue
Consumer-type tariff: residential ₹4.5, commercial ₹7.5, shown as range
L07
DT Input Tampered
DT input vs feeder topology → metering team, not inspector
L08
Cold Start New DTs
Proxy forecast · max MEDIUM until 21-day native window completes
L09
Prepaid Depletion
meter_type field · balance depletion excluded from anomaly logic
L10
Inspector Gaming
Outcome embedded in closure · quality score per inspector
L11
Demo Build Risk
SHAP pre-cached · core demo = 2 screens · buffer in build plan

## Slide 12
Technology Stack — 100% Open Source, 100% Pip-Installable
No GPU required for demo · Cross-platform relative paths · All packages standard pip
Data Layer
· pandas + numpy (data engine)
· scipy.stats.linregress (core)
· pyarrow (6 parquet files)
· json + os (configs)
ML / Forecasting
· lightgbm (LGBMRegressor)
· statsmodels STLForecast
· scikit-learn (MAE metric)
· shap (TreeExplainer, pre-cached)
Intelligence
· rolling windows (pandas)
· 4-condition gate logic
· log1p queue scoring
· relative threshold step detection
Demo UI
· streamlit (dashboard)
· plotly Scattermap (map)
· plotly.express (scatter)
· plotly.graph_objects (charts)
Persistence
· 6 parquet data files
· JSON registry + SHAP cache
· 15 pickle LightGBM models
· relative paths (cross-OS)
Code Quality
· ast.parse() syntax checks
· 12-point fix verification
· Zero hardcoded Linux paths
· Zero hardcoded UI values

## Slide 13
The Model Classifies.
The Inspector Decides.
The Revenue Recovers.
The System Improves.
₹5.2L+
Annual Recoverable
Revenue
3/3
Anomalies
Detected
5
Priority
Classes
11
Loopholes
Fixed
0
Silent
Failures
Lead Dev: Yeshwanth Reddy P G · Researcher: Aditya S · Debugger: Bezaleel Paul N
CMR University · 1st Year CSE / AI-ML · PAN IIT AI for Bharat 2026 · Theme 8 · BESCOM Smart Meters · Taj Yeshwantpur, Bengaluru · May 16, 2026